Qbox User Guide

version 1.52.0

2010-04-16

François Gygi
fgygi@ucdavis.edu
http://eslab.ucdavis.edu

# Introduction
Qbox is a First-Principles Molecular Dynamics code. It can be used to compute the electronic structure of atoms, molecules, solids and liquids within the Density Functional Theory (DFT) formalism. It can also be used to perform first-principles molecular dynamics (FPMD) simulations using forces computed within DFT. Qbox computes the solutions of the Kohn-Sham equations using a plane-wave basis set and norm-conserving pseudopotentials. It can perform constant-temperature and/or constant-pressure simulations.
# Qbox distribution
Qbox is distributed in source form under the GPL license, and in executable form for specific platforms. For source distribution see http://eslab.ucdavis.edu/software/qbox . Qbox has been built and run on the following combinations of platforms and systems:
1. AMD Opteron 270 - Infinipath / CentOS /Rocks
2. Intel Xeon x86_64/ Fedora8
3. BlueGene/L SDSC, LLNL, ANL
4. IBM p655 Series, Datastar SDSC
5. Teragrid Mercury
6. Teragrid Cobalt
7. Teragrid Tungsten
8. BlueGene/P, ANL
9. Cray XT4 (NERSC franklin)
 Some precompiled executables are available at http://eslab.ucdavis.edu .
# Basic Qbox operation
## Starting Qbox
On most platforms, Qbox is started using the mpirun command. On a Linux platform using the mpich implementation of MPI, the command is
mpirun -np <ntasks> qbox_exec input_file > output_file

The input file contains a list of commands that are read and executed by Qbox. The output file created by Qbox is a valid and well formed XML document. It can be used to extract various diagnostic information after the run is completed. During a Qbox run, the output file can be used to track the progress of the simulation.
## Qbox commands
When used in interactive mode, Qbox prints a prompt
[qbox]

and waits for the user to type a command. When used in batch mode, Qbox reads input from an input file. Output is written on standard output (stdout) and can be redirected to a file. A Qbox input file consists of a sequence of Qbox commands with one command per line. Qbox commands are
angle	compute the angle formed by three atoms
atom	define an atom
compute_mlwf	compute maximally localized Wannier functions
constraint	manage constraints on atomic positions
distance	compute the distance between two atoms
fold_in_ws	fold atoms into the Wigner-Seitz cell
help	print a short message about the use of a command
kpoint	add or remove k-points
list_atoms	print a list of currently defined atoms
list_species	print a list of currently defined atomic species
load	load a sample from a file previously saved
move	move atoms
plot	generate a plot file with atoms and/or charge density
print	print the value of a Qbox variable
quit	exit Qbox
randomize_wf	add random noise to the wavefunction coefficients
rescale_v	rescale atomic velocities
reset_vcm	set the velocity of the center of mass to zero
run	run MD or electronic optimization steps
save	save a sample on a file for later use
set	assign a value to a Qbox variable
species	define a new atomic species
status	print a summary of the current state
strain	impose a strain on the sample
torsion	compute the dihedral angle defined by four atoms
!(shell escape) execute a shell command

Commands and their syntax are described in detail in the Section “Qbox commands”.
If a command is read on input and is not in the above list, Qbox interprets it as the name of an input script and attempts to open a file having that name in the current working directory. If the file can be opened and is readable, Qbox starts interpreting each line of that file as its input. Qbox scripts can be nested. At the end of a script, Qbox returns to the previous script level and continues to read commands. At the end of the topmost level script, Qbox exits.
Unix commands can be issued within a Qbox input sequence using a shell escape “!” character at the beginning of a line. For example, the line

[qbox] !date

invokes the Unix date command.
Comments can be inserted in Qbox input by inserting a '#' character at the beginning of each comment line

[qbox] # print the list of all atoms
[qbox] list_atoms

Comments can also be added at the end of a command line by inserting a “#” character where the comment starts

[qbox] list_atoms # get a list of all atoms
## Qbox variables
Calculation parameters such as the plane-wave energy cutoff are specified using Qbox variables. Qbox variables can be set using the set command. Their value can be printed using the print command. For example the command
set ecut 24

sets the variable ecut to the value 24. This causes the plane wave basis set to be resized to include all plane waves with a kinetic energy not exceeding 24 Rydberg. Other Qbox variables can be set similarly. The Qbox variables are

atoms_dyn	ionic dynamics control variable
cell	dimensions of the unit cell
cell_dyn	unit cell dynamics control variable
cell_lock	control of allowed unit cell motions
cell_mass	fictitious mass of the unit cell
charge_mix_coeff	mixing coefficient for charge density update
charge_mix_ndim	Anderson dimension for charge density mixing
charge_mix_rcut	Kerker screening for charge density update
debug	debug parameters (not for normal use)
dt	time step (a.u.)
ecut	plane wave energy cutoff (Ry)
ecutprec	energy cutoff of the preconditioner (Ry)
ecuts	energy cutoff of the confinement potential
emass	fictitious electronic mass (for CP dynamics)
ext_stress	externally applied stress (GPa)
fermi_temp	Fermi temperature (K)
nempty	number of empty states
net_charge	net charge of the system
nrowmax	maximum size of process grid columns
ref_cell	dimensions of the reference unit cell
stress	stress control variable
thermostat	thermostat control variable
th_temp	thermostat temperature (K)
th_time	thermostat time constant (a.u.)
th_width	thermostat width (K)
wf_diag	wavefunction diagonalization control variable
wf_dyn	wavefunction dynamics control variable
xc	exchange-correlation control variable

Qbox variables have a default value. Refer to the Section “Qbox variables” for details.
## Structure of a Qbox script
A Qbox script starts with commands defining the sample being simulated. For example, the sequence of commands
set cell 20 0 0 0 20 0 0 0 20
species silicon silicon.xml
atom Si1 silicon 3.000 0.000 0.000
atom Si2 silicon 0.000 2.000 0.000
atom Si3 silicon -3.000 0.000 0.000
atom Si4 silicon 0.000 -2.000 0.000

defines a sample in a cubic unit cell of size 20 a.u. (Bohr radii). The sample consists of a 4-atom silicon cluster. The definition of the species “silicon” is given in the file silicon.xml. A species definition document contains all the information needed to describe an atomic species, including the pseudopotential used to represent the electron-ion interaction. Species can also be defined by a URI as in the following command
species carbon http://www.example.org/species/carbon.xml

Species definition documents are XML documents that follow the syntax defined by the http://www.quantum-simulation.org XML Schema definition.
# Examples of use of Qbox
## Electronic structure of a Si4 cluster
The following example shows how to use Qbox to compute the electronic ground state of a silicon 4-atom cluster. Approximate input atomic coordinates are used. The electronic ground state is computed using 200 iterations of the preconditioned steepest descent algorithm with Anderson acceleration (PSDA).
# example: electronic structure of si4
set cell 20 0 0 0 20 0 0 0 20
species silicon silicon.xml
atom Si1 silicon 3.500 0.000 0.000
atom Si2 silicon 0.000 2.000 0.000
atom Si3 silicon -3.000 0.000 0.000
atom Si4 silicon 0.500 -2.000 0.000
set ecut 12
set wf_dyn PSDA
set ecutprec 4
randomize_wf
run 0 200
## Structure optimization
The following example shows how to optimize the structure of a Si4 cluster. The electronic ground state is computed using 200 iterations of the preconditioned steepest descent algorithm (PSDA). The structure is then optimized using 50 steps of the steepest descent with Anderson acceleration (SDA) algorithm. Five steps of electronic optimization are performed before each ionic step.
# example: structure optimization of Si4
set cell 20 0 0 0 20 0 0 0 20
species silicon silicon.xml
atom Si1 silicon 3.500 0.000 0.000
atom Si2 silicon 0.000 2.000 0.000
atom Si3 silicon -3.500 0.000 0.000
atom Si4 silicon 0.000 -2.000 0.000
set ecut 12
set wf_dyn PSDA
set ecutprec 4
randomize_wf
run 0 200
# start structure optimization
set atoms_dyn SDA
set dt 100
run 50 5
## Molecular dynamics simulation
The following example shows how to perform a Born-Oppenheimer molecular dynamics simulation. The electronic ground state is first computed using 200 iterations of the preconditioned steepest descent algorithm (PSDA). A Born-Oppenheimer MD is then done by running 50 ionic steps with 5 electronic iterations at each ionic step.
# example: molecular dynamics of si4
set cell 20 0 0 0 20 0 0 0 20
species silicon silicon.xml
atom Si1 silicon 3.500 0.000 0.000
atom Si2 silicon 0.000 2.000 0.000
atom Si3 silicon -3.500 0.000 0.000
atom Si4 silicon 0.000 -2.000 0.000
set ecut 12
set wf_dyn PSDA
set ecutprec 4
randomize_wf
run 0 200
# start molecular dynamics
set atoms_dyn MD
set dt 40
run 50 5

## Saving and restarting a simulation
The following example shows how to save the simulation sample on a file at the end of a simulation and how to restart from the saved file. In the first script, the electronic ground state is computed using 200 iterations of the preconditioned steepest descent algorithm (PSDA). A Born-Oppenheimer MD is then done by performing 50 ionic steps with 5 electronic iterations at each ionic step. The sample is saved at the end of the first script on file si4.xml. In the second script, the sample is loaded from the restart file and 50 additional MD steps are performed.

# script 1: electronic ground state and 50 MD steps
set cell 20 0 0 0 20 0 0 0 20
species silicon silicon.xml
atom Si1 silicon 3.500 0.000 0.000
atom Si2 silicon 0.000 2.000 0.000
atom Si3 silicon -3.500 0.000 0.000
atom Si4 silicon 0.000 -2.000 0.000
set ecut 12
set wf_dyn PSDA
set ecutprec 4
randomize_wf
run 0 200
# perform 10 MD steps
set atoms_dyn MD
set dt 40
run 50 5
# save the sample
save si4.xml

# script 2: restart from saved sample and
# perform 50 MD steps
load si4.xml
set wf_dyn PSDA
set ecutprec 4
set atoms_dyn MD
run 50 5
# save the sample
save si4.xml

## Changing energy cutoff on the fly
The size of sample files can become large when simulating large systems. Although Qbox uses a parallel I/O algorithm to save sample data, the process of writing data to a file can be slow, especially on platforms that do not offer a parallel file system. This problem can be alleviated by saving the sample with reduced resolution for wavefunctions. The value of the variable ecut can be changed using the set ecut command at any time during the simulation. When the value of ecut changes, Qbox interpolates wavefunctions onto the plane wave basis defined by the new value. The size of the sample file can be reduced by changing the value of ecut to a small value before using the save command. When loading a sample that was saved with reduced resolution, the original resolution can be restored by first redefining the value of ecut and then reoptimizing the wavefunctions.
The ability to change energy cutoff on the fly is also useful to accelerate a ground state calculation by starting the calculation at low cutoff and gradually increasing the cutoff to the final desired value. This procedure can be compared to the full approximation scheme of the multigrid method.

## Using Qbox in client-server mode
Qbox can be used in client-server mode. This means that Qbox can run on one computer as a server that “listens” to commands being sent from another computer. Commands can be sent by a user, but also by another program (the “client”, or “driver”). This allows for extensions of the functionality of Qbox in which the client and the server interact to achieve a result that is not easy to get with the conventional approach of submitting a fixed input file to Qbox. A Qbox driver (or “Qbox application”) program sends commands to Qbox by writing them to a file. Qbox reads the commands, executes them, and produces an output file. The client code can then read the output file, process it, and send the next commands to Qbox. Synchronization of this process is implemented through the creation (or destruction) of a file (the “lock” file) that signals that the output (or input) file is ready for use.
Qbox is run in client-server mode by invoking it as follows
mpirun -np <ntasks> qbox_exec -server input_file output_file

The sequence of operations in client-server mode is described below:

Qbox:
1. Create a new file output_file.
2. Read commands from input_file and execute them until the end of file is reached. Write the output on output_file. After executing the last command in input_file, close output_file and create a file named input_file.lock to signal that Qbox is ready for more commands.
3. Wait for the file input_file.lock to be removed by the driver.
4. Go to 1)

Client:
1. Wait for the file input_file.lock to appear.
2. Open the file output_file and read its contents.
3. Analyze the contents and decide what course of action to take.
4. Open the file input_file and overwrite it with new commands.
5. Close input_file.
6. Remove input_file.lock to signal that the file input_file is ready.
7. Go to 1)

Note that in server mode, Qbox only exits when it reads the quit command. When reaching the end of file in input, Qbox does not exit but creates the lock file and then waits for the client to remove it. It then starts reading the input file again.

The contents of output_file form a valid XML document, i.e. The XML header is repeated every time the output file is rewritten. This allows one to process each output file using XML tools, such as e.g. XSLT scripts.

A client can manage multiple copies of Qbox running in server mode. In that case, multiple copies of Qbox must be launched with different input and output file names. For example:

mpirun -np <ntasks> qbox_exec -server in0 out0 &
mpirun -np <ntasks> qbox_exec -server in1 out1 &
mpirun -np <ntasks> qbox_exec -server in2 out2 &

The client must then write on the files in0, in1, in2, and read output from the files out0, out1, out2. This allows for simulations involving multiple samples, such as replica exchange dynamics, nudged-elastic-band (NEB) simulations, or path-integral molecular dynamics.
# Qbox commands
### angle
NAME
angle --compute the value of the angle defined by the positions of three atoms
SYNOPSIS
angle atom1 atom2 atom3
DESCRIPTION
The angle command prints the value of the angle formed by the three atoms given as arguments. The names atom1, atom2 and atom3 must refer to the names of atoms currently defined in the sample.
RELATED INFORMATION
list_atoms, distance, torsion
### atom
NAME
atom --add an atom to the current sample
SYNOPSIS
atom name species x y z [vx vy vz]
DESCRIPTION
The atom command adds an atom to the current sample. The name argument can be any character string but must differ from all the other names of atoms in the current sample. The species argument must refer to an atomic species previously defined using the species command. The position of the atom is specified by its coordinates x, y, z in atomic units (Bohr). Optionally, the velocity of the atom can be specified by its components vx, vy, vz in atomic units (Bohr/atomic-unit-of-time). (One atomic-unit-of-time is 0.02418885 fs).
RELATED INFORMATION
list_atoms, species
### compute_mlwf
NAME
compute_mlwf –compute maximally localized Wannier functions
SYNOPSIS
compute_mlwf
DESCRIPTION
The compute_mlwf command transforms the current wavefunctions into maximally localized Wannier functions following the algorithm in Computer Physics Communications 155 , p. 1 (2003) and a one-sided iterative Jacobi algorithm for simultaneous diagonalization. The position of Wannier centers and the corresponding spreads are printed on output. The value of the electronic, ionic and total dipole are printed. The iterative methods stops when the decrease of the spread is sufficiently small between two iterations, or when a maximum number of iterations is reached. In that latter case, the compute_mlwf command can be issued again to try to improve the convergence of the spread minimization. After execution of the compute_mlwf command, the wavefunctions are maximally localized.
RELATED INFORMATION

### constraint
NAME
constraint --manage constraints on atomic positions
SYNOPSIS
constraint define position constraint_name atom1
constraint define distance constraint_name atom1 atom2 distance [velocity]
constraint define angle constraint_name atom1 atom2 atom3 angle [velocity]
constraint define torsion constraint_name atom1 atom2 atom3 atom4 angle [velocity]
constraint list
constraint delete constraint_name
constraint enforce
constraint set constraint_name value [velocity]
DESCRIPTION
The constraint command is used to manage the constraint set. Constraints can be of the following types: position, distance, angle or torsion. Constraints are added to the constraint set using the “constraint define” command. They can be removed from the set using the “constraint delete” command. A list of constraints can be printed using the “constraint list” command. Some constraints have an associated value that can be modified using the “constraint set” command. The atom names used in the constraint command must refer to atoms previously defined using the atom command. All constraints have a name, which allows for selective removal of constraints and for individual modification of the constraint values.
constraint define position constraint_name atom1
Define a position constraint on atom atom1. This locks the atom into its current position.
constraint define distance constraint_name atom1 atom2 distance [velocity]
Define a distance constraint on atoms atom1 and atom2. If a velocity argument is given, the value of the distance will change at each time step of the simulation at a rate specified by the velocity argument. The velocity must be given in [Bohr/(a.u. time)].
constraint define angle constraint_name atom1 atom2 atom3 angle [velocity]
Define an angle constraint on atoms atom1, atom2 and atom3. If a velocity argument is given, the value of the angle will change at each time step of the simulation at a rate specified by the velocity argument. The velocity must be given in [degree/(a.u. time)].
constraint define torsion constraint_name atom1 atom2 atom3 atom4 angle [velocity]
Define a torsion (or dihedral) constraint on atoms atom1, atom2, atom3 and atom4. If a velocity argument is given, the value of the angle will change at each time step of the simulation at a rate specified by the velocity argument. The velocity must be given in [degree/(a.u. time)].
constraint list
Print a list of all currently defined constraints.
constraint delete constraint_name
Remove the constraint constraint_name from the constraint set.
constraint enforce
Modify atomic positions so as to enforce all constraints using the SHAKE algorithm.
constraint set constraint_name value [velocity]
Modify the value of a constraint, and optionally its velocity. This applies to the distance, angle and torsion constraints only, for which the value is distance, angle and angle, respectively.

RELATED INFORMATION
list_atoms, angle, distance, torsion
### distance
NAME
distance --print the distance between two atoms
SYNOPSIS
distance atom1 atom2
DESCRIPTION
The distance command prints the value of the distance separating two atoms. In periodic samples, the printed distance is not necessarily the minimal distance between the two atoms.
RELATED INFORMATION
angle, torsion
### fold_in_ws
NAME
fold_in_ws –fold all atoms within the Wigner-Seitz cell
SYNOPSIS
fold_in_ws
DESCRIPTION
The fold_in_ws command moves atoms by multiples of the unit cell lattice vectors so that all atoms are withing the Wigner-Seitz cell.
RELATED INFORMATION

### help
NAME
help --print a brief help message about a command
SYNOPSIS
help [command]
DESCRIPTION
The help command prints a short description of the command given as an argument. When used without arguments, prints a list of valid commands.
RELATED INFORMATION
### kpoint
NAME
kpoint –define and manage the set of k-points used in the calculation of the electronic structure.
SYNOPSIS
kpoint list
kpoint add kx ky kz weight
kpoint delete kx ky kz
DESCRIPTION
The kpoint command is used to add and delete k-points to the set of k-points used in the electronic structure calculation. The kpoint is defined by a vector on the basis of the reciprocal lattice vectors. If reciprocal lattice vectors are b1 b2 and b3 the k-point defined by the numbers (kx, ky, kz) on the command line is kx * b1 + ky * b2 + kz * b3. For example, the X point of the Brillouin Zone for an FCC lattice is specified as kx=0.5, ky=0.5, kz=0.0.
The list of all currently defined k-points can be printed using the command kpoint list.
The sum of the weight arguments must add up to 1.0. This is currently not checked by Qbox.
Some k-points can be defined with zero weight. In that case, the electronic wavefunctions and eigenvalues are computed at these points, but they are not included in the calculation of the charge density.
By default, Qbox starts with a k-point set containing a single k-point: k=(0,0,0) (the Γ point) with a weight of 1.0. When defining a k-point set, it is necessary to first delete the Γ point before defining other k-points. This is due to two possible reasons:
1. The desired k-point set does not contain the Γ point.
2. The desired k-point set contains the Γ point, but with a weight different from 1.0. In this case, the Γ point must be deleted and then added in order to be defined with the correct weight. The only way to change the weight of a k-point is to delete it and define it again.
Qbox does not perform any symmetrization of the charge density to reduce the number of k-points to the irreducible wedge of the Brillouin Zone. The full set of k-points must be defined (except for the k, -k symmetry, i.e. If k is included in the set, then -k need not be included).
Modifying the k-point set erases all wavefunctions. It is not possible to modify the k-point set after running a calculation or after loading a sample without resetting the wavefunctions.
Note: When deleting a kpoint, the arguments kx, ky, kz are compared to the coordinates of the k-points currently defined. Since comparisons of floating point numbers are unreliable, the kpoint delete command will delete any k-point located within a radius of 10-6 of the vector (kx, ky, kz). Similarly, when adding a new k-point, the kpoint add command will exit without defining the new k-point and print a warning message if a previously defined k-point is located within a radius of 10-6 of the new kpoint.
EXAMPLE
Define a set of 8 k-points for a simple cubic or orthorhombic cell. This k-point set is equivalent to doubling the cell in all three directions
kpoint delete 0 0 0
# Gamma point
kpoint add 0.0 0.0 0.0 0.125
# X point
kpoint add 0.5 0.0 0.0 0.125
kpoint add 0.0 0.5 0.0 0.125
kpoint add 0.0 0.0 0.5 0.125
# R point
kpoint add 0.5 0.5 0.5 0.125
# M point
kpoint add 0.5 0.5 0.0 0.125
kpoint add 0.5 0.0 0.5 0.125
kpoint add 0.0 0.5 0.5 0.125

Define the X and L points in the Brillouin Zone of a FCC lattice, with zero weight:
# a1 = (a/2, a/2, 0)
# a2 = (0, a/2, a/2)
# a3 = (a/2, 0, a/2)
# b1 = (2*pi/a) ( 1.0, 1.0, -1.0)
# b2 = (2*pi/a) (-1.0, 1.0, 1.0)
# b3 = (2*pi/a) ( 1.0, -1.0, 1.0)
# X point
# X = (2*pi/a) ( 1.0, 0.0, 0.0 ) = 0.5 * ( b1 + b3 )
kpoint 0.5 0.0 0.5 0.0000
# L point
# L = (2*pi/a) ( 0.5, 0.5, 0.5 ) = 0.5 * ( b1 + b2 + b3 )
kpoint add 0.5 0.5 0.5 0.0000

RELATED INFORMATION
### list_atoms
NAME
list_atoms --print a list of atoms currently defined in the sample
SYNOPSIS
list_atoms
DESCRIPTION
The list_atoms command prints a list of all atoms currently defined.
RELATED INFORMATION
list_species, atom
### list_species
NAME
list_species --print a list of all species currently defined
SYNOPSIS
list_species
DESCRIPTION
The list_species command prints a list of all species currently defined. For each species, the parameters of the corresponding pseudopotential are printed.
RELATED INFORMATION
list_atoms, species
### load
NAME
load --load a sample from an XML sample document
SYNOPSIS
load URI
DESCRIPTION
The load command loads a simulation sample defined in an XML document provided by the URI argument. The URI can be a local file, in which case Qbox will open and read the file. If URI is a URL (e.g. http://www.quantum-simulation.org/examples/samples/ch4.xml) Qbox will download the document from the corresponding web site.
Qbox sample documents must conform to the XML Schema definition provided at
 http://www.quantum-simulation.org

RELATED INFORMATION
save
### move
NAME
move --change the position of an atom
SYNOPSIS
move atom to x y z
move atom by dx dy dz
DESCRIPTION
The move command moves an atom to an absolute position specified by x, y, z or by a relative displacement specified by dx, dy, dz. Positions or displacements must be given in atomic units (Bohr)
RELATED INFORMATION

### plot
NAME
plot –generate a plot file with atoms and/or charge density or orbitals
SYNOPSIS
plot filename
plot -density filename
plot -wf n filename
plot -wf nmin nmax filename
DESCRIPTION
The plot command creates a plot file to be viewed with another rendering program such as VMD or XcrysDen. The type of output file generated depends on the arguments given to the plot command.
- plot filename
  This command generates an xyz file containing atomic positions only.
- plot -density filename
  This command generates a file in cube format containing the atomic positions and the total charge density
- plot -wf n filename
  This command generates a file in cube format containing the n-th wavefunction
- plot -wf nmin nmax filename
  Generate a file in cube format containing the sum of the squares of the amplitudes of the wavefunctions nmin to nmax inclusive
The plot command is only working for wavefunctions at the Γ point.

RELATED INFORMATION

### print
NAME
print --print the current value of a Qbox variable
SYNOPSIS
print variable
DESCRIPTION
The print command prints the current value a Qbox variable. For a list of variables, see the section “Qbox variables”.
RELATED INFORMATION
set
### quit
NAME
quit --exit Qbox
SYNOPSIS
quit
DESCRIPTION
The quit command exits Qbox without saving any information about the sample. To save the current sample, see the save command.
RELATED INFORMATION
save
### randomize_wf
NAME
randomize_wf --add a random perturbation to electronic wavefunctions
SYNOPSIS
randomize_wf [amplitude]
DESCRIPTION
The randomize_wf command adds random numbers to the Fourier coefficients of the electronic wavefunction. The amplitude argument can be used to change the intensity of the perturbation.
The randomize_wf command is used at the beginning of an electronic structure calculation when the symmetry of the atomic coordinates is high. In such situations, the iterative algorithms used to compute the electronic ground state can converge to saddle points of the energy functional instead of true minima. Using randomize_wf introduces a slight symmetry breaking which is sufficient to avoid high-symmetry saddle points.
RELATED INFORMATION
### rescale_v
NAME
rescale_v –rescale atomic velocities
SYNOPSIS
rescale_v scaling_factor
DESCRIPTION
The rescale_v command rescales the velocity of all atoms by a common factor defined by the scaling_factor argument.
 RELATED INFORMATION
### reset_vcm
NAME
reset_vcm --reset the velocity of the center of mass to zero
SYNOPSIS
reset_vcm
DESCRIPTION
The reset_vcm command modifies the velocity of all atoms so as to ensure that the velocity of the center of mass is zero. The current value of the velocity of the center of mass is printed by the status command
RELATED INFORMATION

### run
NAME
run --update electronic wavefunctions and/or atomic positions
SYNOPSIS
run [-atomic_density] niter
run [-atomic_density]niter nitscf
run [-atomic_density]niter nitscf nite
DESCRIPTION
The run command starts a simulation in which atomic positions and/or electronic states are updated. The algorithms used to update the atomic positions and electronic states are determined by the variables atoms_dyn and wf_dyn. The parameters are defined as follows
-atomic_density The first self-consistent iteration is started using a charge density made of a superposition of atomic charge densities.
- niter	The number of ionic steps to be performed, i.e. steps during which atomic positions are updated. This number can be zero if only electronic wavefunction updates are desired.
- nitscf	The number of self-consistent electronic iterations. The charge density is updated at the beginning of each self-consistent iteration.
- nite	The number of electronic iterations performed between updates of the charge density
The run command can be used in the following ways
- run niter
  Perform niter ionic steps. Before each ionic step, the electronic states are updated once, and the charge density is updated (i.e. both parameters nitscf and nite default to 1). Using “run 0” computes the total energy without modifying the electronic wavefunction.
- run niter nitscf
  Perform niter ionic steps. Before each ionic step, the charge density is updated nitscf times. Before each update of the charge density, the electronic states are updated once (i.e. the parameter nite defaults to 1.
- run niter nitscf nite
  Perform niter ionic steps. Before each ionic step, the charge density is updated nitscf times. Before each charge density update, the electronic states are updated nite times.

Example 1
run 0 100
is used to perform 100 self-consistent electronic optimization steps. Only electronic optimization is performed. This the most common way of computing the electronic ground state.
Example 2
run 50 10
is used to perform 50 ionic steps, with 10 charge density updates before each ionic step. Before each charge density update, the electronic states are updated once.

Example 3
run 50 5 10
is used to performed 50 ionic steps. The charge density is updated 5 times before each ionic step. The electronic states are updated 10 times before each charge density update.
If the variable cell_dyn is not set to LOCKED, the unit cell parameters are updated each time the atomic positions are updated. In that case, the stress variable must be set to ON so that the stress tensor is computed before the cell parameters are updated.
Atomic positions are updated before the charge density and electronic states are updated. As a consequence, the atomic positions and the electronic structure are consistent at the end of a run command.
RELATED INFORMATION
atoms_dyn, wf_dyn
### save
NAME
save --save the current sample into a file
SYNOPSIS
save filename
DESCRIPTION
The save command saves the current sample into a file in XML format. The format used conforms to the XML Schema defined at http://www.quantum-simulation.org. The information saved includes the dimensions of the unit cell, atomic positions and velocities, the electronic wavefunction, and optionally the time derivative of the wavefunction.
RELATED INFORMATION
load
### set
NAME
set --assign a value to a Qbox variable
SYNOPSIS
set variable value [value ...]
DESCRIPTION
The set command assigns the value(s) value to the variable variable. Some variables (e.g. cell) are multivalued, in which case the set command requires multiple arguments.
RELATED INFORMATION
print
### species
NAME
species --define a new atomic species and add it to the list of currently known species
SYNOPSIS
species name URI
DESCRIPTION
The species command defines a new atomic species under the name name. The newly defined species is added to the list of currently known species. The definition is read from the given URI. If the URI is a local file, Qbox opens and reads it. If the URI is a URL (e.g.
http://www.quantum-simulation.org/examples/species/hydrogen_pbe.xml) Qbox downloads the species definition from the corresponding web site. The species definition document must conform to the species XML Schema definition given at http://www.quantum-simulation.org
RELATED INFORMATION
list_species, atom
### status
NAME
status --print status of the current sample
SYNOPSIS
status
DESCRIPTION
The status command prints a brief summary of the characteristics of the current sample.
RELATED INFORMATION

### strain
NAME
strain –apply strain on the system
SYNOPSIS
strain [-atomsonly] [-inverse] uxx uyy uzz uxy uyz uxz
DESCRIPTION
The strain command modifies the shape of the unit cell and modifies the atomic positions to impose a strain defined by the component of the symmetric strain tensor u. Using the -inverse flag causes the inverse transformation to be applied. Using -atomsonly changes the postitions of atoms without affecting the unit cell
RELATED INFORMATION

### torsion
NAME
torsion --print the value of the torsion angle defined by the positions of four atoms
SYNOPSIS
torsion atom1 atom2 atom3 atom4
DESCRIPTION
The torsion command prints the value of the angle (dihedral) defined by the four atoms given as arguments. The names atom1, atom2 atom3 and atom4 must refer to the names of atoms currently defined in the sample.
RELATED INFORMATION
list_atoms, angle, distance
### ! (shell escape)
NAME
! (shell escape) --execute a Unix command from withing Qbox
SYNOPSIS
! command [arguments]
DESCRIPTION
The ! command executes the command given as an argument in a Unix shell.
RELATED INFORMATION
# Qbox variables
### atoms_dyn
NAME
atoms_dyn --atom dynamics control variable
DESCRIPTION
The atoms_dyn variable determines the algorithm used to update atomic positions during a simulation. The following values are allowed:
- LOCKED: Ionic forces are not computed and atomic positions are not updated. This is the default.
- SD: Steepest Descent. Ionic forces are computed and atomic positions are updated using the steepest descent algorithm
vec R (t+dt) = vec R(t) + { dt^2 } over m vec F (t)
where F is the force, m is the ionic mass and dt is the time step (see variable dt).
- SDA: Steepest Descent with Acceleration. A line minimization algorithm is used to find a minimum satisfying the Wolfe conditions before changing the descent direction. Using this algorithm requires a full calculation of the electronic ground state at each ionic step, i.e. nitscf > 1 in the run command.
- CG: Conjugate Gradient. A line minimization algorithm is used to find a minimum satisfying the Wolfe conditions before changing the descent direction. The Polak-Ribiere formula is used to update descent directions. Using this algorithm requires a full calculation of the electronic ground state at each ionic step, i.e. nitscf > 1 in the run command. Using this algorithm requires a full calculation of the electronic ground state at each ionic step, i.e. nitscf > 1 in the run command.
MD: Molecular dynamics. Ionic forces are computed and ionic positions are updated using the Verlet algorithm
vec R (t+dt) = 2 vec R(t) - vec R (t-dt) + { dt^2 } over m vec F (t)
This algorithm can be used to perform either Born-Oppenheimer molecular dynamics (using nitscf > 1 in the run command) or Car-Parrinello molecular dynamics (nitscf=1). See also the wf_dyn variable.
BMD: Blocked Molecular dynamics. This algorithm updates ionic positions according to the MD algorithm (Verlet), but velocities are reset to zero every time the total energy increases. This algorithm is used to optimize geometry. It requires a full calculation of the electronic ground state at each ionic step, i.e. nitscf > 1 in the run command.
ALLOWED VALUES
LOCKED, SD, SDA, CG, MD, BMD
RELATED INFORMATION
dt
### cell
NAME
cell --unit cell parameters
DESCRIPTION
The cell variable contains the coordinates of the three lattice vectors vec a_1, vec a_2, vec a_3 defining the unit cell. The unit cell is defined using the set command with the following arguments
set cell a1x a1y a1z a2x a2y a2z a3x a3y a3z
The lattice vectors vec a_1, vec a_2, vec a_3 form the columns of the 3x3 lattice parameter matrix A
A = left ( matrix{a_{11} # a_{12} # a_{13} ## a_{21} # a_{22} # a_{32} ## a_{31} # a_{32} # a_{33}} right )
The default value of all cell parameters is zero.
ALLOWED VALUES
positive real numbers
RELATED INFORMATION
ref_cell
### cell_dyn
NAME
cell_dyn --cell dynamics control variable
DESCRIPTION
The cell_dyn variable determines the algorithm used to update the unit cell during a simulation. The following values are allowed:
- LOCKED: The unit cell is not updated. This is the default.
- SD: Steepest Descent. The unit cell is updated using the computed stress tensor and the steepest descent algorithm
a_{ij} (t+dt) = a_{ij} (t) + { dt^2 } over m_%OMEGA %OMEGA left ( %sigma (t) - %sigma^{ ext} (t) right ) A(t)
where %sigma (t) is the stress tensor, %sigma^{ext} (t) is the externally applied stress (variable ext_stress), %OMEGA is the volume of the unit cell, m_%OMEGA is the mass of the unit cell (variable cell_mass), A is the 3x3 lattice parameter matrix (see cell variable) and dt is the time step (variable dt).
ALLOWED VALUES
LOCKED, SD
RELATED INFORMATION
cell, ref_cell, cell_lock
### cell_lock
NAME
cell_lock --cell dynamics constraints control variable
DESCRIPTION
The cell_lock variable is used to restrict the possible changes of the unit cell parameters. The allowed values are
- OFF:	No restriction on the unit cell parameters are enforced. This is the default.
- A:	The lattice vector vec a_1 is fixed.
- B:	The lattice vector vec a_2 is fixed.
- C:	The lattice vector vec a_3 is fixed.
- AB:	The lattice vectors vec a_1 and vec a_2 are fixed.
- AC:	The lattice vectors vec a_1 and vec a_3 are fixed.
- BC:	The lattice vectors vec a_2 and vec a_3 are fixed.
- ABC:	All lattice vectors are fixed. This is equivalent to cell_dyn = LOCKED.
- S:	The shape of the unit cell is preserved. Lattice vectors can change length but not	direction.
- AS:	The lattice vector vec a_1 is fixed and the shape of the unit cell is preserved.
- BS:	The lattice vector vec a_2 is fixed and the shape of the unit cell is preserved.
- CS:	The lattice vector vec a_3 is fixed and the shape of the unit cell is preserved.
- ABS:	The lattice vectors vec a_1 and vec a_2 are fixed and the shape of the unit cell is preserved.
- ACS:	The lattice vectors vec a_1 and vec a_3 are fixed and the shape of the unit cell is preserved.
- BCS:	The lattice vectors vec a_2 and vec a_3 are fixed and the shape of the unit cell is preserved.
- R:	The aspect ratio of the unit cell is preserved. All lattice vectors are rescaled by the	same constant.
ALLOWED VALUES
OFF, A, B, C, AB, AC, BC, ABC, S, AS, BS, CS, ABS, ACS, BCS, R
RELATED INFORMATION
cell, cell_dyn, cell_mass
### cell_mass
NAME
cell_mass --mass of the unit cell
DESCRIPTION
The cell_mass variable is the mass of the unit cell in atomic units (in which the mass of a carbon atom is 12.0). The default value is 10000.
ALLOWED VALUES
positive real values
RELATED INFORMATION
cell, cell_dyn
### charge_mix_coeff
NAME
charge_mix_coeff --charge density mixing coefficient
DESCRIPTION
The charge density mixing coefficient is used to update the electronic charge density during self-consistent iterations (see charge_mix_ndim). The default value is 0.5. Smaller values can be used to accelerate the convergence of self-consistent iterations in metallic systems.
ALLOWED VALUES
real values in the interval [0,1]
RELATED INFORMATION
charge_mix_rcut, charge_mix_ndim
### charge_mix_ndim
NAME
charge_mix_ndim –dimension of Anderson acceleration of charge mixing
DESCRIPTION
The charge_mix_ndim parameter n determines how many previous charge density corrections are used in the Anderson acceleration of the charge mixing scheme. The new input charge density is computed according to
%rho_{"in"}^{(k+1)} = overline %rho + %alpha overline %f
where %alpha is the charge mixing coefficient (charge_mix_coeff) and overline f is the least-squares residual in the subspace spanned by the n previous charge density corrections
overline %f = %delta%rho^{(k)} + sum from{i=1} to{n} %theta_i ( %delta%rho^(k-i) - %delta%rho^(k) )
where %delta%rho^(k) = %rho_{"out"}^(k) - %rho_{"in"}^(k) is the difference between the output and input charge density of the self-consistent iteration k, and
overline%rho = %rho_{"in"}^(k) + sum from{i=1} to{n} %theta_i (%rho_{"in"}^(k-i) - %rho_{"in"}^(k) )
The coefficients %theta_i are chosen so as to minimize ldline overline f rdline _2^2 in a row-weighted least squares sense.
The weight used in the LS calculation is the Kerker screening function
w (bold G) = {bold G^2 + q_0^2}over{bold G}^2
where q_0 = 2 %pi / r_c and r_c is the charge mixing cutoff radius (charge_mix_rcut).
The default value of n is 3.
SPECIAL VALUES
Using n=0 leads to simple mixing: %rho_{"in"}^(k+1) = %rho_{"in"}^{(k)} + %alpha (%rho_{"out"}^{(k)} - %rho_{"in"}^{(k)} )
ALLOWED VALUES
non-negative integers
RELATED INFORMATION
charge_mix_rcut, charge_mix_coeff
### charge_mix_rcut
NAME
charge_mix_rcut --charge mixing cutoff radius
DESCRIPTION
The charge_mix_rcut variable is used to define the range of the Coulomb interaction in the Kerker screening function used in the charge density mixing scheme (see charge_mix_ndim).
The default value of charge_mix_rcut is 10 a.u.
If charge_mix_rcut is set to zero, no screening is used.
ALLOWED VALUES
positive real numbers
RELATED INFORMATION
charge_mix_ndim , charge_mix_ndim
### debug
NAME
debug --debug parameters
DESCRIPTION
The debug variable is used to pass debug parameters to Qbox. It is not intended for normal use.
ALLOWED VALUES
character strings
RELATED INFORMATION

### dt
NAME
dt --simulation time step
DESCRIPTION
The dt variable is the simulation time step in atomic units of time (1 a.u. of time = 0.02418885 fs). The default value is 3 a.u.
ALLOWED VALUES
non-negative real numbers
RELATED INFORMATION
atoms_dyn, wf_dyn, cell_dyn
### ecut
NAME
ecut --plane-wave basis energy cutoff
DESCRIPTION
The ecut variable defines the size of the plane wave basis used to define the electronic wavefunctions. It must given in Rydberg units. The wavefunction plane wave basis consists of all plane waves having a kinetic energy smaller than E_cut . The charge density and the total potential are described using a larger basis set that includes all plane waves with a kinetic energy smaller than 4 E_cut . The default value of ecut is zero, in which case the plane wave basis contains one basis function--the plane wave of wavevector { bold G } = 0 .
ALLOWED VALUES
non-negative real numbers
RELATED INFORMATION
### ecutprec
NAME
ecutprec --preconditioning energy cutoff
DESCRIPTION
The ecutprec variable defines the energy cutoff used in the preconditioner for electronic structure optimization. Corrections to the electronic wavefunctions are preconditioned in Fourier space using a diagonal preconditioning matrix K whose elements are defined by
k_ij = %delta_ij k(G) newline k(G) = left lbrace matrix {1 over { 2 E_cut^prec } # alignl 1 over 2 G^2 < E_cut^prec ## 1 over 2 E # alignl 1 over 2 E >= E_cut^prec } right none
The value of ecutprec must be given in Rydberg units. Preconditioning is only used if the wf_dyn variable is set to either PSD or PSDA. If ecutprec = 0, no preconditioning is used. The default value of ecutprec is zero. Effective preconditioning is achieved with ecutprec < ecut/2 or ecutprec < ecut/4. Small values of ecutprec (< 5 Ry) can lead to instabilities.
ALLOWED VALUES
positive real numbers smaller than or equal to ecut.
RELATED INFORMATION
ecut, wf_dyn
### ecuts
NAME
ecuts --energy cutoff for stress confinement potential
DESCRIPTION
The ecuts variable defines the energy cutoff used in a confinement potential in Fourier space. The confinement potential is used when computing the stress tensor with variable cell size in order to ensure constant resolution as the unit cell changes size. The confinement energy is
E_conf = 1 over 2 sum from{n,{bold G}} lline c_{n{bold G}} rline ^2 G^2 f(G)
where
f(g) = f_s left ( 1 - 1 over { 1 + exp((G^2/2-E_cut^s)/%sigma_s) } right )
f_s = 2 and %sigma_s = 1 over 2 .
The default value of ecuts is zero, in which case the confinement potential is not used.
For a detailed description of the use of confinement potentials in constant pressure simulations, see
1. P. Focher, G. L. Chiarotti, M. Bernasconi, et al. Structural Phase-Transformations Via 1St-Principles Simulation, Europhys. Lett. 26 (5): 345-351 (1994).
2. M. Bernasconi, G. L. Chiarotti, P. Focher, et al. First-Principle Constant-Pressure Molecular-Dynamics, Journal Of Physics And Chemistry Of Solids 56 (3-4): 501-505 (1995).

ALLOWED VALUES
positive real numbers smaller than or equal to ecut
RELATED INFORMATION
stress, cell_dyn
### emass
NAME
emass --fictitious electronic mass for Car-Parrinello simulations
DESCRIPTION
The emass variable defines the fictitious electronic mass used in Car-Parrinello simulations. The default value is zero, in which case the fictitious electronic mass used in the calculation is m_e = 2 E_cut dt^2 . The value of emass is only relevant if the variable wf_dyn is set to MD (i.e. if the wavefunction dynamics is Car-Parrinello). It is ignored otherwise.
ALLOWED VALUES
positive real values
RELATED INFORMATION
wf_dyn
### ext_stress
NAME
ext_stress --external stress
DESCRIPTION
The ext_stress variable determines the value of the externally applied stress. The ext_stress variable must be set using the following syntax
set ext_stress %sigma_xx %sigma_yy %sigma_zz %sigma_xy %sigma_yz %sigma_xz
where the values of the elements of the stress tensor must be given in GPa units. The external stress can be positive or negative. The default value is zero.
ALLOWED VALUES
real numbers
RELATED INFORMATION
stress
### fermi_temp
NAME
fermi_temp --Fermi temperature for fractionally occupied states
DESCRIPTION
The fermi_temp variable determines the value of the Fermi temperature used in the calculation of occupation factors for fractionally occupied states. The value must be given in Kelvin. The default value is zero.
ALLOWED VALUES
non-negative real numbers
RELATED INFORMATION
nempty
### nempty
NAME
nempty --number of empty electronic states
DESCRIPTION
The nempty variable determines the number of electronic states that are included in the calculation in addition to the number of states needed to accomodate the total number of electrons. If nempty is non-zero, the eigenvalues and eigenvectors of the Kohn-Sham hamiltonian are computed at each electronic iteration and the charge density is recomputed from the eigenvectors using a Fermi distribution. The default value is of nempty is zero.
ALLOWED VALUES
non-negative integers
RELATED INFORMATION
fermi_temp
### net_charge
NAME
net_charge --net charge of the system
DESCRIPTION
The net_charge variable is used to control the total amount of electronic charge in the calculation. If net_charge = 0, the total number of electrons is determined from the sum of the valence charges given in the species definition files and the system is neutral. If net_charge = -1, an extra electron is added to the system. If net_charge = 1, an electron is removed from the system. The default value is zero.
ALLOWED VALUES
integers
RELATED INFORMATION

### nrowmax
NAME
nrowmax --maximum number of process grid rows
DESCRIPTION
The nrowmax variable determines the shape of the process grid used in parallel calculations. It is used to optimize performance when large numbers of parallel tasks are used. The default value is 32.
ALLOWED VALUES
positive integers
RELATED INFORMATION

### ref_cell
NAME
ref_cell --reference unit cell
DESCRIPTION
The ref_cell variable determines the size of the reference unit cell. The reference unit cell is used in constant pressure calculations to ensure constant resolution of the basis set as the unit cell changes size. The unit cell must always be enclosed in the reference unit cell during a constant pressure calculation.
ALLOWED VALUES
positive real numbers
RELATED INFORMATION
cell
### stress
NAME
stress --stress calculation control variable
DESCRIPTION
The stress variable determines whether the stress tensor is calculated. The possible values are ON and OFF. The default is OFF.
ALLOWED VALUES
ON, OFF
RELATED INFORMATION
ext_stress, cell_dyn
### thermostat
NAME
thermostat --thermostat control variable
DESCRIPTION
The thermostat variable determines what type of thermostat is used for constant temperature simulations. The choices are
- OFF: No thermostat is used. This is the default.
- SCALING: Scaling of velocities. At each MD step, the velocities of all atoms are rescaled as
  v_i = v_i ( 1 - %eta dt )
  where
  %eta = 1 over %tau tanh { T - T_ref } over { %DELTA }
  %tau is the thermostat time constant (variable th_time), T is the instantaneous temperature computed from the ionic kinetic energy, Tref is the thermostat reference temperature (variable th_temp), and %DELTA is the thermostat temperature width (variable th_width).
- ANDERSEN: Andersen thermostat. The atoms are subjected to random collisions with particles drawn from a Maxwell distribution of velocities with temperature Tref. The collision frequency is 1/%tau where %tau is given by the variable th_time (see H. C. Andersen, J. Chem. Phys. 72, 2384 (1980)).
- LOWE: Lowe thermostat. Pairs of atoms are subjected to random collisions with a particle drawn from a Maxwell distribution of velocities with temperature Tref. The collision frequency is 1/%tau where %tau is given by the variable th_time . The Lowe thermostat is similar to the Andersen thermostat but conserves total momentum (see C. P. Lowe, Europhys. Lett. 47, 145 (1999)).
- BDP: Bussi-Donadio-Parrinello thermostat. The stochastic thermostat described by Bussi, Donadio and Parrinello in J. Chem. Phys. 126, 014101 (2007) is used. The parameter %tau used in the BDP paper is the value of the variable th_time. The value of the variable th_width is ignored. When using the BDP thermostat, the value of <econst> printed on output corresponds to the conserved energy described in the above paper.
ALLOWED VALUES
OFF, SCALING, ANDERSON, LOWE, BDP
RELATED INFORMATION
th_temp, th_time, th_width,
### th_temp
NAME
th_temp --thermostat reference temperature
DESCRIPTION
The th_temp variable determines the thermostat reference temperature. The default is zero. See thermostat.
ALLOWED VALUES
non-negative real numbers
RELATED INFORMATION
th_time, th_width, thermostat
### th_time
NAME
th_time --thermostat time constant
DESCRIPTION
The th_time variable determines the thermostat time constant. The time constant is a measure of the time over which the thermostat adjusts the temperature. See thermostat for details. The value of th_time must be given in atomic units of time. The default value is 5000 a.u. (~ 120 fs).
ALLOWED VALUES
positive real numbers
RELATED INFORMATION
th_temp, th_width, thermostat
### th_width
NAME
th_width --thermostat temperature window
DESCRIPTION
The th_width determines the value of the thermostat temperature width. See thermostat details. The value of th_width must be given in Kelvin units. The default value is 100 K.
ALLOWED VALUES
positive real numbers
RELATED INFORMATION
th_temp, th_time, thermostat
### wf_diag
NAME
wf_diag --diagonalization control variable
DESCRIPTION
The wf_diag variable determines whether eigenvectors and/or eigenvalues of the hamiltonian are computed after each optimization of the electronic structure. The choices are
- T: True. Eigenvalues and eigenvectors are computed. Eigenvalues are printed on output in eV units.
- F: False. Eigenvalues and eigenvectors are not computed. This is the default.
- EIGVAL: Eigenvalues only. The eigenvalues are computed and printed, but eigenvectors are not computed.
- MLWF: Maximally localized Wannier Functions (MLWFs) are computed.
- MLWFC: The position of MLWF centers is computed and printed but MLWFs are not computed.
  If empty states are added to the calculation (variable nempty > 0) the eigenvalues and eigenvectors are always computed.
ALLOWED VALUES
T, F, EIGVAL,MLWF,MLWFC
RELATED INFORMATION

### wf_dyn
NAME
wf_dyn --wavefunction dynamics control variable
DESCRIPTION
The wf_dyn variable determines which algorithm is used to update the wavefunctions during electronic structure optimization. The choices are
SD:	Steepest Descent. This the default. Wavefunctions are updated as follows:
%psi^(k+1) = %psi^(k) - %alpha H %psi^(k)
where
%alpha = left lbrace matrix { 1 over { 2 E_cut } # alignl m_e = 0 ## dt^2 over m_e # alignl m_e > 0 } right none
and me is the fictitious electronic mass (variable emass). By default, me=0.
PSD:	Preconditioned Steepest Descent. Wavefunctions are updated as follows:
%psi^(k+1) = %psi^(k) - %alpha K P_{{}ortho{}} H %psi^(k)
where K is a preconditioning matrix
k_ij = %delta_ij k(G) newline k(G) = left lbrace matrix {1 over { 2 E_cut^prec } # alignl 1 over 2 G^2 < E_cut^prec ## 1 over 2 E # alignl 1 over 2 E >= E_cut^prec } right none
and P_{{}ortho{}} = I - sum_i left lline %psi_i right rangle left langle %psi_i right rline is a projector on the orthogonal complement of the subspace spanned by all wavefunctions. The preconditioning matrix depends on the value of E_cut^prec (variable ecutprec).
- PSDA:	Preconditioned Steepest Descent with Anderson acceleration. Wavefunctions are updated as with the PSD option, and convergence is accelerated by the Anderson scheme (D. G. Anderson, JACM 12, No 4, pp. 547-560 (1965)).
- JD: Jacobi-Davidson. Wavefunctions are updated using a preconditioned Jacobi-Davidson algorithm.
- MD: Molecular Dynamics. Wavefunctions are updated using the Car-Parrinello scheme
%psi_i^(k+1) = 2 %psi_i^(k) - %psi_i^(k-1) - dt^2 over m_e H %psi_i^(k)+ sum_j %LAMBDA_ij %psi_j^(k)
where holonomic constraints are used to enforce orthogonality.
LOCKED. Wavefunctions are not updated.
ALLOWED VALUES
SD, PSD, PSDA, JD, MD, LOCKED
RELATED INFORMATION
other variables or commands
### xc
NAME
xc --exchange-correlation functional control variable
DESCRIPTION
The xc variable determines which exchange-correlation functional is used in the electronic structure calculation. The choices are
- LDA:	Local Density Approximation, Ceperley-Alder data. This is the default.
- PBE:	Perdew-Burke-Ernzerhof GGA functional.
ALLOWED VALUES
LDA, PBE
RELATED INFORMATION